## Slide 1: UNIT-3 Number System
Number System Conversion
Any to decimal
Logic gates and Boolean Algebra
Compliments
decimal to Any
1’s Complement
SOP and POS
SOP Form
B-G
2’s complement
Code Conversion
G-B
Excess-3
BCD code
Binary Addition and Subtraction
Logic gates
Boolean Algebra Rules
Simplification of Boolean Algebra
POS Form
Octal and Hexadecimal into Binary
Kmap
K-map Rule
Simplification using Kmap

## Slide 2
Today’s Highlights
Number System Conversion
Any to decimal
Binary to Decimal
Octal to Decimal
Hexadecimal to Decimal
Decimal to Any
Octal and Hexadecimal into Binary
Decimal to binary
Decimal to Octal
Decimal to Hexadecimal
Octal to Hexadecimal
Hexadecimal to octal

## Slide 5: IS (𝟐𝟖𝟗𝟏)8 is octal ???
Explanation Slide
MSB and LSB
5
A) True
B) False

## Slide 6: IS (𝟐𝟖𝟗𝟏) 𝟏𝟔 is Hexadecimal? ??
Explanation Slide
MSB and LSB
6
A) True
B) False

## Slide 7: Types of Number System: COMPARISON

## Slide 9: Number Conversion: Decimal to Other Base
1. Decimal to Binary Conversion:
Step 1: Continuously divide by 2 until quotient is either 0 or 1.
Step 2: Note down the remainder corresponding to each division.
Step 3: The pattern of 1’s and 0’s at the remainder column represented from bottom to top represents the equivalent binary number.

## Slide 10
 |  | QUICK QUIZ (POLL)
Q. a) | 28 10 in binary is: 110110 | 
b) | 11011 | 
c) | 11000 | 
d) | 11100 | 

## Slide 11: Try Yourself
Q1. Convert the following into Binary equivalents?
a) 247 10
b) 27 10

## Slide 12: Number System: Base Conversion with Fractions
1. Decimal to Binary Conversion:
𝐶𝑜𝑛𝑣𝑒𝑟𝑡(0.6875)10 to binary?
Step 1: Continuously multiply by 2 until fractional part is 0. Or Multiply by 2 until you observe that the fractional part is either repeating or never ending.
Step 2: Note down the integer part corresponding to each multiplication
Step 3: The pattern of 1’s and 0’s at the integer column represented from top to bottom represents the fractional part into an equivalent binary number.

## Slide 13: Ex2 :Convert decimal number 0.75 into binary form
Reading the carries from top to bottom, the result is 0.11.
Thus, the binary equivalent of (0.75)10 is (0.11)2
Steps: 1. Multiply the fractional decimal number by 2. 2. Integral part of resultant decimal number will be first digit of fraction binary number. 3.Repeat step 1 using only fractional part of decimal number and then step 2.

## Slide 14: Try Yourself
Q1. Convert the following into Binary equivalents?
a) 0.65 10
Attempt Poll:
𝟑𝟕. 𝟔𝟓𝟔𝟐𝟓 𝟏𝟎
---- Binary
a) 100101.10101
b) 101101.10111
c) 110101.11101

## Slide 15: Explanation Slide

## Slide 16: Ex 3: Convert (177)10 to octal equivalent
Answer = 261
Note: 0 6 2 the answer is read from bottom to top, the same as with the binary case.

## Slide 17: Ex4: Convert (0.1640625)10 to octal
Therefore, 0.164062510 = (0.124)8.

## Slide 18: Ex 4: Convert decimal number 122810 into hex
122810 = 4CC16

## Slide 19: QUICK QUIZ (POLL)
Q. Convert the following to octal: 305 10
a) 440
b) 441
c) 460
d) 461
POLL
(0.6875)10…….( )8
A.45
B.54
C.55
D5.5
FRACTION part

## Slide 20: Ex 6: Convert (152.25)10 Hexadecimal
Step 1: Divide the number 152 and its successive quotients with base 16.
(152)10=(98)16
Step 2: Now perform the multiplication of 0.25 and successive fraction with base 16.
(0.25)10=(4)16
hexadecimal number of the decimal number 152.25 is 230.4.

## Slide 21: QUICK QUIZ (POLL)
Q. Convert the following to hexadecimal: 7825 10
a) 𝐵321
b) 1E91
c) 123A
d) E240
FRACTION part : (0.760)10…….( )16 A)DF120
B)C28F5 C)CA8F5 D)DA8F6

## Slide 22: Number System: Base Conversion
1. Binary to Decimal Conversion:
Step 1: Multiply with the powers of 2𝑛
where n=0,1,2,3,… starting from the LSB.
Step 2: Add all the decimal numbers corresponding to the coefficients.
Step 3: The sum obtained would be the equivalent decimal number representation of the given binary number.
LSB
MSB
Integer part

## Slide 23: Number System: Base Conversion
Binary to Decimal Conversion:
Step 1: Multiply with the powers of 2𝑛
where n=0,1,2,3,… starting from the LSB.
Step 2: Add all the decimal numbers corresponding to the coefficients.
Step 3: The sum obtained would be the
equivalent | decimal |  | number
representation | of the | given | binary
number. |  |  | 
𝑅𝑒𝑠𝑢𝑙𝑡: (357)10
𝐵𝑖𝑛𝑎𝑟𝑦: (101100101)2
2nd
example

## Slide 24: QUICK QUIZ (POLL)
Q. Convert the following binary number to decimal:
a) 11
01011
2
b) 35
c) 15
d) 10

## Slide 25: Number System: Base Conversion with Fractions
1. Binary to Decimal Conversion:
Step 1: Multiply with the powers of 2−𝑛
where n=1,2,3,… starting from the MSB.
Step 2: Add all the decimal numbers corresponding to the coefficients.
Step 3: The sum obtained would be the
decimal
of the given
number binary
equivalent representation number.
𝐶𝑜𝑛𝑣𝑒𝑟𝑡(0.1011)2 to decimal?
Fraction part

## Slide 26: Number System: Base Conversion with Fractions
1. Binary to Decimal Conversion:
Step 1: Multiply with the powers of 2−𝑛
where n=1,2,3,… starting from the MSB.
Step 2: Add all the decimal numbers corresponding to the coefficients.
Step 3: The sum obtained would be the
equivalent | decimal |  | number
representation | of the | given | binary
number. |  |  | 
𝐶𝑜𝑛𝑣𝑒𝑟𝑡(0.11011)2 to decimal?

## Slide 27: Try Yourself
Q1. Convert the following into Decimal equivalents?
a) 01101.10011 2
b) 1010111.001101 2
Home assignments
Share on lpu live

## Slide 28
Q1. Convert the following into Decimal equivalents? (1011.10011)2
A) (11.59735)10
B) (10.59735)10
C) (11.59375)10
D) (10.59375)10
QUICK QUIZ (POLL)

## Slide 29: Number System: Base Conversion
2. Octal to Decimal:
• The method is quite similar to the transformation of any binary number to decimal, the only difference is that in this case the 2 will be replaced by 8 and everything else i.e. the methods will remain same.
• We have to start multiplying the digits of the number from LSB side with increasing powers of 8 staring from 0 and finally summing up all the products.

## Slide 30: QUICK QUIZ (POLL)
Q. Convert the following to decimal:
a) 280.00123
431.32 8
b) 281.40625
c) 421.40625
d) 431.4343

## Slide 31
Convert (6432)8 into decimal
(.32 )8------( )10

## Slide 32: Number System: Base Conversion
3. Hexadecimal to Decimal:
• The method is quite similar to the transformation of any binary number to decimal, the only difference is that in this case the 2 will be replaced by 16 and everything else i.e. the methods will remain same.
• we have to start multiplying the digits of the number from LSB side with increasing powers of 16 staring from 0 and finally summing up all the products.

## Slide 33: QUICK QUIZ (POLL)
Q. Convert the following to decimal: 3𝐹𝐵 a) 1210
16
b) 1019
c) 4821
d) 1101

## Slide 34: QUICK QUIZ (POLL)
Q. Convert the following to decimal: A9.8 16
a) 121.0
b) 101.9
c) 169.5
d) 110.1

## Slide 35: Binary to Octal Conversion
Step1: To convert from binary to octal, start grouping the bits in groups of 3 from the right end
Step2: Write the equivalent octal for the 3-bit binary.
Step3: Add 0’s on the left to adjust the groups.

## Slide 36: Octal to Binary Conversion

## Slide 37: Binary to Hexadecimal Conversion
Step1: To convert from binary to octal, start grouping the bits in groups of 4 from the right end
Step2: Write the equivalent octal for the 3-bit binary.
Step3: Add 0’s on the left to adjust the groups.

## Slide 38: Ex-1 Convert (110111110111.1100)2 to hexadecimal
The hexadecimal equivalent of (110111110111.1100)2 is (DF7.C)16.
EX-2: Convert (1110111001101.111011)2 to hexadecimal
The hexadecimal equivalent of the given binary number is (1DCD.EC)16.

## Slide 39: Hexadecimal to Binary Conversion
Ex-1: The given hexadecimal number is 6FD16. Find out its binary form.
616 = 01102
F16 = 11112
D16 = 11012
Ans: 6FD16 = 0110 1111 11012

## Slide 40: Octal to Hexadecimal Conversion
Step 1 − Convert each digit of the given octal number to its equivalent binary of 3-bits.
Step 2 − Make groups of 4 bits each of the obtained binary number.
Step 3 − Convert each 4-bit binary group to its equivalent hexadecimal.
EX 1: Convert (742.35)8 to hexadecimal.
Hexadecimal equivalent of the given octal number is (1E2.74)16.

## Slide 41: POLL
Q1.(3CFB.2E)16---------(?)8
A) (36363.134)8
B) (36373.134)8
C) (37373.134)8
Q2. (574.32)8-------------(?)16
A) (17C.68)16 B) (17D.78)16 C) (17E.78)16

## Slide 42: Practice Question
Convert (25)10 in Binary
What is equivalent value of (278)10 in Binary?
Convert decimal number 0.125 into binary form
Convert decimal number 65.16 into binary form
Convert (82.523)10 to octal equivalent up to 3 decimal places.
Convert 756210 to hex
Convert (524.26)10 to hexadecimal.
Convert hexadecimal number 8F4E9A16 to its binary form.

## Slide 43
Disadvantages of Number System
Complex Arithmetic Operations
Error-Prone Data Entry
Unstable StaHuman Readability Issueste
Increased Hardware Requirements
Inefficient Memory Usage
How to Overcome
this problems ??