## Slide 1
Today’s Highlights
Code Conversion

## Slide 2: Need for Code Conversion
Inter-System Compatibility
Simplified Circuit Design
Error Detection and Correction
Human-Readable Output
Optimization of Memory and Processing
Application-Specific Requirements
Need for Code Conversion

## Slide 3: Code Conversion
Decimal to BCD code
1.In the BCD numbering system, the given decimal number is segregated into chunks of four bits for each decimal digit within the number.
2. Each decimal digit is converted into its direct binary form (usually represented in 4-bits).
Decimal Number | BCD | Excess 3 code
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100

## Slide 4
Ex-1: Convert (123)10 in BCD
From the truth table above, 1 -> 0001 2 -> 0010
3 -> 0011 Thus, BCD becomes -> 0001 0010 0011
Ex-2: Convert (324)10 in BCD
(324)10
Again from the truth table above, 3 -> 0011 2 -> 0010 4 -> 0100 thus, BCD becomes -> 0011 0010 0100

## Slide 5: QUICK QUIZ (POLL)
Q. What is the BCD representation of the decimal number 57?
  A. 0101 0111
  B. 0110 0111
  C. 0101 0110
  D. 1001 0110

## Slide 6
Ex-1
Decimal to Excess-3 Conversion
Ex-2 Decimal number 31
Home assignment

## Slide 7: QUICK QUIZ (POLL)
Q. What is the Excess-3 code for the decimal number 9?
A. 1010
B. 1100
C. 1001
D. 1110

## Slide 8: Try Yourself
Q1. What is the BCD (Binary-Coded Decimal) representation of the decimal number 75?
Q2. Which of the following is the Excess-3 code for the decimal number 26?
Home assignments
Share on lpu live

## Slide 9: Binary to Gray Code Conversion

## Slide 10: Gray Code to Binary Conversion

## Slide 11: QUICK QUIZ (POLL)
Q. What is the Gray code equivalent of the binary number 1011?
A. 1100
B. 1110
C. 1001
D. 0111

## Slide 12: QUICK QUIZ (POLL)
Q. What is the binary equivalent of the Gray code 1101?
A. 1000
B. 1011
C. 1111
D. 1100

## Slide 13: Try Yourself
Q1. Convert the decimal number 187 into BCD (Binary-Coded Decimal) code.
Q2. Convert the decimal number 56 into Excess-3 code.
Q3. Convert the decimal number 23 into Gray Code.
Home assignments
Share on lpu live

## Slide 14
Why 1’s and 2’s Complement Needed??