## Slide 1: LOGIC GATE, BOOLEAN ALGEBRA

## Slide 2
Today’s Highlights
Logic Gates (Truth Table)
Rules of Boolean Algebra
Simplification of Functions

## Slide 3: Need for Logic gates
Signal Processing
Data Storage
Arithmetic & Computation
Decision Making
Simplified Circuit Design

## Slide 4
Logic Gates
Universal Gates
Basic Gates
Arithmetic Gates
AND
OR
NOT
NAND
NOR
XOR
XNOR

## Slide 5
LLogic Gate
IC 7408
IC 7404
IC 7432

## Slide 6
NAND and NOR gates are called Universal gates called universal
IC 7400
IC 7402

## Slide 7
IC 7486
IC 747266

## Slide 8
AND
OR
NOT
XOR
Poll

## Slide 9
AND
OR
NOT
XOR
Poll

## Slide 10
AND
OR
XOR
XNOR
Poll

## Slide 11
The output of an AND gate with three inputs, A, B, and C, is HIGH when ________. A. A = 1, B = 1, C = 0 B. A = 0, B = 0, C = 0 C. A = 1, B = 1, C = 1 D. A = 1, B = 0, C = 1
QUICK QUIZ (POLL QUESTION)

## Slide 12: Rules of Boolean Algebra
S.no | Rule Name | OR law | AND law
1 | Null element | A+1=1 | A.0=0
2 | Identity law | A+0=A | A.1=A
3 | Idempotent Law | A+A=A | A.A=A
4 | Complement Law | A+A’=1 [controlling pin] | A.A’=0 [controlling pin]
5 | Commutative law | A+B=B+A [order does not matter] | A.B=B.A [order does not matter]
6 | Associative law | A+(B+C)=(A+B)+C | A.(B.C)=(A.B).C
7 | Distributive law | A+(B.C)=(A+B).(A+C) | A.(B+C)=(A.B)+(A.C)
Also known as switching algebra
8 | Absorption law | A+AB=A | A.(A+B)=A

## Slide 13: Rules of Boolean Algebra
9 | Double Inversion law | A’’=A | 
10 | Redundant Literal Rule (RLR) | A+A’B=A+B or A’+AB=A’+B or A’+AB’=A’+B’ or A +A’B’=A+B’ | 
11 | Consensus Theorem | AB+A’C+BC=AB+A’C | 
De Morgan’s First Law Implementation using Logic Gates
NAND = Bubbled OR gate
NOR=bubbled AND
De Morgan’s Second Law Implementation using Logic Gates

## Slide 14: Need for De Morgan’s Law
Simplification of Boolean Expressions
Inversion of Logic Gates
Gate Optimization
Designing with Negative Logic
Conversion Between NAND and NOR
Fault Tolerance and Redundancy
Easier Circuit Design and Implementation
Universality in Digital Systems

## Slide 15
De’ Morgan Laws:

## Slide 16
Which of the following Boolean theorem is incorrect? A. A + A = A
B. A + 1 = 1
C. A + 0 = A
D. A + A’ = 0
QUICK QUIZ (POLL QUESTION)

## Slide 17
DUAL of the function

## Slide 18: Simplification

## Slide 19: Quick Poll
Simplify the expression
Z=X’Y
Z =X+Y’
Z=XY
Z=X+Y

## Slide 20: Logic Gate Implement with NAND-NOR

## Slide 21
Home assignment XNOR using NAND and XOR using NOR send on LPU live
NAND and NOR as Universal Gates

## Slide 22
Combination of Gates

## Slide 23
Draw circuit for
Exercise
Combination of Gates

## Slide 24
Practice Question:
Simplification using Boolean Algebra

## Slide 25: Simplification using Boolean Algebra
Practice Question:
Simplify the following Boolean expression:
Home Assignment
AB
A’B
AB+AC’
A’B+AC’

## Slide 26: Advantages of Boolean Algebra
[1]
[2]
[3]
To obtain simpler expression
To reduce the number of gates in the circuit
To reduce the number of inputs in the circuit
[4]
To reduce complexity
[5]
To reduce cost.

## Slide 27
Minimum number of two input NAND gates required to implement XOR function is: A. 3 B. 4 C. 5 D. 6
QUICK QUIZ (POLL QUESTION)

## Slide 28
Limitation OF Boolean Algebra and Expressions
1. Lack of Representation for Negative Values
2. Limited to Binary States
3. Complexity in Simplification
4. Lack of Direct Representation for Arithmetic Operations
5. Handling of Multiple Inputs and Outputs
6. No Support for Continuous Data
How to Overcome Said problem