## Slide 3
Fundamentals of Electrical Laws, Semiconductor Devices, and its Applications
UNIT-1

## Slide 4: Electrical Circuit

## Slide 5: Charge and Current
Charge:
Charge is an electrical
property of the atomic particles of a matter.
S.I Unit: Coulomb (C)
Symbol: Q
Current: Rate of change of charge.
OR
Continuous flow electrons in an electrical circuit.
S.I Unit: Ampere (A) Symbol: I
of

## Slide 6: Charge and Current
Mathematically,
𝐼 =
𝑑𝑄
𝑑𝑡
𝑡
𝑜𝑟 𝑄 = ∫ 𝐼. 𝑑𝑡
𝑡0
Or, in simple terms:
𝐼 =
𝑄
𝑇
So, 1 Ampere = 1 coulomb/ 1 second.

## Slide 7: QUICK QUIZ (Poll 1)
1 Coulomb is same as:
Watt /sec
Ampere/sec
Joule-sec
Ampere-sec

## Slide 8: QUICK QUIZ (Poll 2)
The total charge entering the terminal is 5𝑠𝑖𝑛4𝜋𝑡 𝑚𝐶. Calculate current at t= 0.5 sec.:
A. 31.2 A
B. 31.2 mA
C. 62.8 mA
D. 62.8 A

## Slide 9: Voltage
It is the energy (Work) required to move a unit charge through a wire in closed path.
S.I Unit: Volt (V) Symbol: V

## Slide 10: Power and Energy
Power: Rate at which the work is done.
OR
Time rate of absorbing or supplying energy
S.I Unit: Watts (W) Symbol: P
Mathematically,
𝑑𝑡 𝑑𝑞 𝑑𝑡
𝑃 = 𝑑𝑊=𝑑𝑊 . 𝑑𝑞 = 𝑉.𝐼
Implies,
𝑃 = 𝑉. 𝐼

## Slide 11: Power and Energy
Energy: Capacity of doing work.
S.I Unit: Joules(J) Symbol: E

## Slide 12: QUICK QUIZ (Poll 3)
Calculate the current ratings of 100 Watt incandescent bulb and 15 Watt LED lamp operated with the domestic supply of 220 Volt?
Bulb = 0.068 A and LED = 0.45 A
Bulb = 0.45 A and LED = 0.068 A
Bulb =0.50 A and LED = 0.068 A
Bulb = 0.50 and LED = 0.68 A

## Slide 13: QUICK QUIZ (Poll 4)
From the previous question, it can be inferred that:
LED consumes 5 times more current than Bulb.
Bulb consumes 5 times more current than LED..
LED consumes 6.6 times more current than Bulb.
Bulb consumes 6.6 times more current than LED.

## Slide 14: Network Components
Active
Passive
Battery
Transistor,
Op-amp,
Diode
VS and CS
Generators
Resistance (R) Capacitance (C) Inductance (L)
Transformers

## Slide 15: Resistance
Resistance: It is an opposition to the flow of current.
S.I Unit: Ohm (Ω)
Symbol: R

## Slide 16: Ohm’s Law
Given by Georg Simon Ohm (1787–1854), a German physicist
Ohm’s law states that the voltage v across a resistor is directly proportional to the current i flowing through the resistor.
Mathematically,
Tool which is used for analysis of circuits: Ohm law, KVL and KCL

## Slide 19
Electrical Circuit
Applications of Ohm’s Law
To find unknown Voltage (V)
To Find unknown Resistance (R)
To Find unknown Current (I)
Can be used to find Unknown Conductance (G)=1/R
Can be used to find unknown Power (P)=VI
Can be used to find unknown conductivity or Resistivity

## Slide 20: Limitations of Ohm’s Law
Ohm’s law holds true only for a conductor at a constant temperature. Resistivity changes with temperature.
Ohm’s law by itself is not sufficient to analyze circuits.
It is NOT applicable to non linear elements, For example, Diodes, Transistors, Thyristors, etc.
This law cannot be applied to unilateral networks.

## Slide 21: Applications of Ohm’s Law

## Slide 22: Poll
Q.1 An electric iron draws 2 A at 120 V. Find its resistance.
Q.2 The essential component of a toaster is an electrical element (a resistor) that converts electrical energy to heat energy. How much current is drawn by a toaster with resistance 15 ohm at 110 V?
40 ohms, 2 Ampere
60 ohms, 7.33 Ampere
20 ohms 8 Ampere
100 ohms 10 Ampere

## Slide 23
Solution:
Solution: I=V/R=110/15=7.333A

## Slide 25: Kirchhoff’s Current Law (KCL)
Algebraic sum of currents entering a node (or a closed boundary) is zero.

## Slide 26: Sign Convention for KCL: Entering Current: Taken as +ve Leaving Current: Taken as -ve
The sum of the currents entering a node is equal to the sum of the currents leaving the node.

## Slide 27: Example for KCL

## Slide 28
Q. Relation between currents according to KCL is
a) i1=i2=i3=i4=i5 b) i1+i4+i3=i5+i2 c) i1-i5=i2-i3-i4 d) i1+i5=i2+i3+i4
Poll

## Slide 29: Kirchhoff’s Voltage Law (KVL)
Algebraic sum of all voltages around a closed path (or loop) is zero.
mathematically,

## Slide 30
Example

## Slide 31: Example
Sum of voltage rises=Sum of voltage drops
Equivalent Circuit

## Slide 32: QUICK QUIZ (Poll 2)
Find voltages 𝑉1 and 𝑉2 in the given circuit:
A. 𝑉1 = 16 𝑉 𝑎𝑛𝑑 𝑉2 = 12 𝑉
B. 𝑉1 = 16 𝑉 𝑎𝑛𝑑 𝑉2 = −8 𝑉
C. 𝑉1 = 8 𝑉 𝑎𝑛𝑑 𝑉2 = −12 𝑉
D. 𝑉1 = −12 𝑉 𝑎𝑛𝑑 𝑉2 = 8 𝑉

## Slide 33
Note: Resistors in series behave as a single resistor whose resistance is equal to the sum of the resistances of the individual resistors.

## Slide 34: Resistors in Parallel .

## Slide 35: How to find Equivalent Resistance for Series-Parallel Combinations

## Slide 38: Note: This rule can be generalized for any number of resistors in series

## Slide 39: Example for Voltage Division Rule

## Slide 43
Simulation based Implementation

## Slide 44
POLL
I1 = 13.33 A
I1 = 23.33 A
I1 = 6.666 A
I1 = 8.666 A

## Slide 45
Simulation based Implementation

## Slide 48
Simulation based Implementation

## Slide 49: Applications of Kirchhoff’s Laws
They can be used to analyze any electrical circuit.
Computation of current and voltage of complex circuits.

## Slide 50: Limitations of Kirchhoff’s Laws
The limitation of Kirchhoff’s both laws is that it works under the assumption that there is no fluctuating magnetic field in the closed loop and the current flows only through conductors and wires.

## Slide 51: Nodes, Branches, and Loops
A branch represents a single element such as a voltage source or a resistor.
A node is the point of connection between
two or more branches.
A loop is any closed path in a circuit
NOTE:
Two or more elements are in series if they exclusively share a single node and consequently carry the same current.
Two or more elements are in parallel if they are connected to the same two nodes and consequently have the same voltage across them.

## Slide 52: QUICK QUIZ (Poll 4)
How many branches, nodes and independent loops are present in the given circuit?
A. b=3, n=5, l=6
B. b=5, n=3, l=6
C. b=5, n=3, l=3
D. b=3, n=5, l=3

## Slide 53
https://be-iitkgp.vlabs.ac.in/List%20of%20experiments.html
E-Resources